## Slide 1
Self-Driving Car for Conference Competition
Team: Zach Copenhaver, Jakob Felts, Fred Levins, Josh Strong
Advisors: Dr. David Hartup, Dr. Bryan Van Scoy
Self driving vehicle
  Travels between points
  Emulates taxi service
This was accomplished by:
Camera feeds process information of track
Mapping of track
Live-updates while the car navigated the track
Vehicle ability to traverse track
Shortest path between nodes
Quick computation time
  g(n) current node cost
  h(n) estimated cost to goal
Vehicle Operations
A* Algorithm
Overview
Node and YOLO feeds
Controls feed
Given start and end destinations
Find shortest path
Run function to travel to next node
Check visual feeds to update position and predict objects
If path has not been completed, continue to next node
QCar Components
NVIDIA Jetson TX2
Four CSI cameras
- 360 degree vision
Intel RGBD camera
LIDAR
Motor encoder
IMU sensor
Expandable IO
References
https://www.quanser.com
https://github.com/vanscoy/qcar
https://opencv.org/about/
https://arxiv.org/pdf/1506.02640.pdf
https://doi.org/10.1109/cvpr.2016.91
https://cocodataset.org/
Visual Representation
Motor Controls
Controls feed set to binary image
  Checks the location of white pixels
  Adjust angle based on error
YOLO trained on COCO dataset
  Cv2 DNN to single pass itemize objects in frames predicts stop signs
  Confidence threshold at 60% and non-max suppression at 40%
Node detection with blue masking
Motors have no bound on maximum speed
  Speed value of 0.066 works best for our cases
Servo angle ranges from -0.5 to 0.5 radians (~28 degrees)
Camera Implementation
f(n) = g(n) + h(n)
v = kff*vt + kp*∆v+∫ki*∆v*dt